## Slide 1: Real-Time Operating Systems
ROS01
Minor Embedded Systems
Week 2
Super loop construct with an ISR
versd@hr.nl
brojz@hr.nl

## Slide 2: Planning ROS01
Week 1: Introduction – Hello World
Week 2: Super loop construct with an ISR
Week 3: Cooperative Scheduling
Week 4: Pre-emptive Scheduling
Week 5: Using TI-RTOS
Week 6: Schedulability Analyses, Priority Assignment
Week 7: Response Time Analyses
Week 8: Finalizing Final Assigment

## Slide 3: Overview
The microcontroller
  History
  Properties of the Cortex M4 CPU
  Interrupt system
  Timers
  Direct Memory Access system
Superloop ‘scheduler’

## Slide 4: ARM History
Started in 1980 as a co-processor
  ARM1 architecture
Latest:
  ARMv9-A architecture (zie bijv. Cortex-A710)
Difference to x86?

## Slide 5: ARM family

## Slide 6: CC3220S

## Slide 7: Cortex M4
ARMv7E-M architecture
  Two modes of operation: Thread (application code) and Handler (exceptions and OS).
    Main SP(MSP) / Process SP (PSP)
  Two privilege levels: Unprivileged and privileged.
  Thumb 2 instructions
    Single cycle integer division/multiply
  Ultra-low power sleep modes
  Atomic bit manipulation (Bit-banding)
  System timer (SysTick)
  Nested Vector Interrupt Controller (NVIC)

## Slide 8: Exceptions – NVIC
Nested Vectored Interrupt Controller
  75 exception sources
  Priority level between -3 to 7 (low number is high priority)
    Priority groups
      group priority (determines preemption)
      sub priority fields (determines order when multiple interrupts are pending)
  Tail-chaining of Exception Handlers
  External Non Maskable Interrupt

## Slide 9: Exception types

## Slide 11: Timers
4 GPTM (16/32)
  two 16 bit counters per module
  OR one 32 bit counter per module
    How long does an overflow take?
  ≈ 4.3e9 ≈ 53.7 s @ 80MHz

## Slide 12: Timers

## Slide 13: Bit-Banding

## Slide 14: Bit-Banding
You should use bit0 in the alias region to change a bit in the bit-band region.

## Slide 15: µDMA
(Bulk) data-transfers without CPU (32 channels)
  Memory <-> Memory
  Memory <-> Peripheral
Several transfer modes
  Basic
  Ping-pong (two alternating buffers to support continuous data flow)
  Scatter-gather
Configuration
  Channel control structures

## Slide 16: Voorbeeld embedded system
T
S
P
Switch
Screen
DAC
ADC
ADC
thermocouple
pressure transducer
heater
pump/valve

## Slide 17: Software Architecture
What is the biggest flaw with this architecture?
  NO control over time
    Not deterministic
      e.g. sample time of T and P depends on execution times
    No response time promises
    Wasting CPU cycles
T
P
S
T
P
S
T
P
S
time
T = temperature control
P = pressure control
S = screen update

## Slide 18: Superloop Construct
Simple, deterministic
Fixed time scheduling using SysTick
Sleep until next SysTick (save energy)
Is it necessary to run all tasks every tick?
T
P
S
T
P
S
time
SysTick
SysTick

## Slide 19: Opdrachten / Verslag
Opdrachten worden niet afgetekend
  Komen wel in het verslag
Je mag om feedback vragen
Verslag
  Bevat code opdrachten
  Uitleg interessante delen
    Bijv. Het adres-masker bij week 1