## Slide 1: Real-Time Operating Systems
ROS01
Minor Embedded Systems
Week 6
Schedulability Analyses, Priority Assignment, RT Analyses (part 1)
versd@hr.nl
brojz@hr.nl

## Slide 2: Planning ROS01
Week 1: Introduction – Blinking leds
Week 2: Super loop construct with an ISR
Week 3: Cooperative Scheduling
Week 4: Pre-emptive Scheduling
Week 5: Using TI-RTOS
Week 6: Schedulability Analyses, Priority Assignment, Response Time Analyses (part 1)
Week 7: Response Time Analyses (part 2)
Week 8: Finalizing Final Assignment

## Slide 3: Free study material (…/minor Embedded Systems/ROS01/Books)
Chapters 3 and 4 of: Ken Tindell and Hans Hansson, Real Time Systems by Fixed Priority Scheduling, Uppsala University, 1997.
Chapter 12 of: Edward A. Lee and Sanjit A. Seshia, Introduction to Embedded Systems, A Cyber-Physical Systems Approach, Second Edition, MIT Press, ISBN 978-0-262-53381-2, 2017.
Original papers:
  C. L. Liu and J. W. Layland, Scheduling Algorithms for Multiprogramming in a Hard Real-Time Environment, JACM, Volume 20, Number1, pages 46 to 61, 1973
  M. Joseph and P. Pandya, Finding Response Times in a Real-Time System, The Computer Journal, Volume 29, Number 5, pages 390-395, 1986

## Slide 4: Task scheduling
In how many ways can you schedule 10 tasks (without preemption)?
Choose one to start with (10 possibilities)
Choose an other to go second (9 possibilities)
…
Total of 10x9x8x7x6x5x4x3x2x1 = 10! = 3628800 possible schedules

## Slide 5: Scheduling tasks
N tasks can be scheduled in N! different ways
  For example 10 tasks: 3628800 possible schedules
  With preemption there are many more possibilities
The chosen schedule must meet all timing requirements
A scheduling scheme (=plan) consists of:
  An algorithm to find the “best” schedule
  A method to predict the “worst-case” behavior of this schedule

## Slide 6: Scheduling tasks… When do we do it?
Static: the schedule is determined before the tasks are started
  All task, their worst-case execution times and deadlines should be known beforehand
  Using response time analysis it is possible to prove that all deadlines are met.
  All response times are predictable!
  Not able to react on “unforeseen” situations
Dynamic: the schedule is determined when the tasks are running.
  Behavior is less predictable
  Can respond dynamically to unforeseen circumstances (e.g. a calculation that takes longer than expected)

## Slide 7: Scheduling Real-Time systems
Almost always a static scheduling method is used
Most commonly used : Preemptive Priority Based scheduling
  On each moment in time the ready task with the highest priority is running
  Scheduling scheme:
    An algorithm to assign a priority to each task
    A method to predict the “worst-case” behavior of this schedule given the assigned priorities and to prove that all timing requirements are met

## Slide 8: Scheduling - Simple model
The number of task is known: N
All tasks are periodical and all period times are known: Ti
The tasks are independent from each other (no synchronization nor communication)
System overhead is neglected
The deadline of each task is equal to it’s period time: Di = Ti
The worst-case execution time of each task is known: Ci
This model is too simple (but difficult enough). Later we will look at realistic models.

## Slide 9: Cyclic executive (Super loop)
The schedule is determined upfront and is explicitly programmed.
Example:
// Set timer to wake-up CPU every 25 ms
while (1) {
sleep_until_wake_up(); a(); b(); c();
sleep_until_wake_up(); a(); b(); d(); e();
sleep_until_wake_up(); a(); b(); c();
sleep_until_wake_up(); a(); b(); d();
}
Taak | T | C
a | 25 | 10
b | 25 | 8
c | 50 | 5
d | 50 | 4
e | 100 | 2
How to determine the schedulability?
How to find a schedule?

## Slide 10: Cyclic executive (Super loop)
Minor cycle = gcd(T1, T2, … Tn). Major cycle = lcm(T1, T2, … Tn).
How to determine the schedulability?
How to find a schedule?
Utilization
U = 10/25+8/25+5/50+4/50+2/100
= 0,92
What is the maximum utilization in the general case?
If Ce = 4 then U = 0,94 and the task set is not schedulable!
signal = systick

## Slide 11: Cyclic executive (Super loop)
Characteristics:
  There are no real tasks, only ordinary functions
  Shared memory can be used for communication without protection (mutex is not needed)
  All T ’s should be a multiple of the minor cycle time
  System is deterministic (predictable)
Issues:
  Tasks with large differences in T ’s result in a large major cycle
  Sporadic tasks (interrupts) can not be included!
  Poorly maintainable, adaptable and expandable
  Determining the schedule is NP-hard! (read: very, very hard)
Alternatives:
  Fixed-Priority Scheduling (FPS)
  Earliest Deadline First (EDF)

## Slide 12: FPS Fixed-priority Pre-emptive Scheduling
Each task runs with a statically determined fixed priority
This priority is determined by the timing requirements of all tasks
The scheduling is preemptive:
  When a task with a higher priority becomes ready, the running task will be preempted (interrupted)

## Slide 13: RMPA = Rate Monotonic Priority Assignment
The period time of a task determines the priority of that task
The shorter the period time the higher the priority
This (simple) method is optimal!
  if some fixed-priority pre-emptive schedule exists, then, the rate monotonic fixed-priority pre-emptive schedule is also feasible

## Slide 14: FPS-RMPA
If this test is true then no deadlines are missed!
If this test is false then maybe some deadlines are missed!
N | Test
1 | U ≤ 1.000
2 | U ≤ 0.828
3 | U ≤ 0.780
4 | U ≤ 0.757
5 | U ≤ 0.743
10 | U ≤ 0.718
infinite | U ≤ 0.693
Utilization based schedulability test:

## Slide 15: FPS-RMPA
Utilization based schedulability test for N → ∞:
L'Hôpital's rule

## Slide 16: FPS-RMPA Schedulability examples
Possibilities:
  Does not meet the test and some deadlines are not met
  Does not meet the test but all deadlines are met
  Does meet the test and all deadlines are met
Meeting the test is sufficient evidence that all deadlines are met. But it is not necessary to satisfy the test in order to meet all deadlines.

## Slide 17: FPS-RMPA Response time analysis
In contrast to the utilization test, this analysis determines the exact response times. So we can say exactly whether all deadlines are met (and by what margin).
Ri is the response time of task i
hp(i) is the set of tasks with a higher priority than task i
Ri appears on the left and the right side of the equation. This equation can not be simply solved. (because the ceiling function is not invertible)

## Slide 18: FPS-RMPA Response time analysis
The response time of the highest priority task is:
All other tasks can be preempted. Their response time is:
Where Ii is the maximum “interference” time. This will occur when all tasks with a higher priority than i start at the same time as task i
The number of times task j with a higher priority than i can preempt task i is given by:
So Ii,j equals:

## Slide 19: FPS-RMPA Response time analysis
The total maximum interference time is the sum of the maximum interference time of every task with a higher priority:
Which can be solved by using a recurrence relation:
Start with
= 0 and continue until:
or

## Slide 20: FPS-RMPA Response time analysis
Further extension of the analysis method is necessary to include:
  Sporadic tasks
  Tasks with D < T
  Interaction between tasks
  Release jitter
  Tasks with D > T
  Release offsets

## Slide 21: FPS-RMPA D < T and Sporadic tasks
D < T:
  Use DMPA instead of RMPA:
  Use the following stop condition in the response time analysis:
Sporadic tasks (interrupts):
  Use the minimum time between two “starts” of this task as the period time T = minimum inter-arrival interval
  For most sporadic tasks D < T

## Slide 22: Homework assignment. ../ros01/Opdrachten/Huiswerk_Week_6.pdf